## Slide 1: Development of analytical methods for the analysis of contaminants in sediment after electro-kinetic treatment
Y. Tian1,2, A. Benamar2, C. Boulangé-Lecomte3, F. Portet-Koltalo1
1 Laboratoire COBRA UMR CNRS 6014, Université de Rouen, 55 rue Saint Germain, 27000 Evreux. 2 Laboratoire LOMC UMR CNRS 6294, Université du Havre, 53 rue Prony, 76058 le Havre. 3 Laboratoire SEBIO UMR I02, Université du Havre, 25 rue Philippe Lebon, CS 80540, 76058 Le Havre
MSPD
Many organic pollutants such as PAHs and PCBs and metal contaminants are accumulated in the sediment
Consequences:
  Damaging aquatic ecosystems
  Toxic for life including human-beings
Aims of researches:
  Develop extraction and analytical methods for these pollutants and their metabolites
  Using electro-kinetic (EK) method for reducing their quantities in sediment
  Organic pollutants:
    16 polycyclic aromatic hydrocarbons (PAHs)
    2 rings 3 rings … 5 rings
    naphthalene phenanthrene benzo[a]pyrene
    7 Polychlorinated biphenyls (PCBs)
  Inorganics: metal contaminants
Introduction
Harbor dredged sediments
Electro-kinetic treatment
Extraction methods
Analytic methods
ICP-AES for metals
GC-MS for PAHs and PCBs
HPLC-Flu/UV for metabolites
Materials & Methods
Results and discussions
GC-MS analysis of PAHs and PCBs
MSPD
Soxhlet
MAE Microwaves
Extraction of soil organic pollutants
MAE (microwave) is more efficient and faster than the traditional Soxhlet method.
Acetone/Toluene or CH2Cl2 = good extracting solvents for PAHs+PCBs
Extraction of real sediment pollutants from Tancarville
Acenaphtalene, fluorene and anthracene > N1 GEODE (< N2), other PAHs < N1.
PCBs < N1.
Metals < N1, but Cd > N2.
Hexane/Acetone
MSPD: matrix solid phase dispersive extraction
Hexane/Acetone 50/50: more efficient
Recovery of PAHs 60% (<71,4% with MAE) and PCBs 90% (>84.5 with MAE).
Effect of solvent volume and combinations of dispersants = not significant
MSPD: simpler and faster than MAE
Conclusion
Perspectives
GC-MS and ICP-AES are adapted to detect different pollutant families in sediment.
Extraction efficiency: MSPD > MAE > Soxhlet.
 MSPD still needs optimization (necessary to introduce surrogate standards to correct results related to poor reproducibility of flow-rates).
HPLC-UV not enough selective to analyse PAHs metabolites
 Coupling UV+fluorescence ? GC-MS after derivatization?
Improving EK treatments using original additive mixtures: biosurfactants + citric acid
Detect PAH metabolites (quinones + hydroxyl-) and reduced PCBs after EK treatment  link with sediment toxicity?
Microcosms tests to monitor natural dissipation of contaminants in Tancarville sediment (comparison with EK treatment efficiency)
4 PAH quinones are separated by C18 RP column.
Resolution is good enough.
Problem: UV detection not enough selective (pics may coincide with other substances)
HPLC-UV analysis for PAH quinones